## Slide 1: Be Free, Little Guardbunny!
Presented at Shmoocon 2016
Kristin Paget
Director of Security Data Cloud
kristin@tombom.co.uk
kpaget@salesforce.com
@kristinpaget

## Slide 2: Much love and many thanks
JP Martin
Henry and the Recursion crew
Salesforce
All the engineers that I've talked at about this :)
My wife and her m4d 5MD 5k1llz <3

## Slide 3: Theory

## Slide 4: What is GuardBunny?
An active RFID shield.
  Conventional shields attempt to block the signal
    Stronger signals saturate and eventually penetrate
  GuardBunny absorbs the signal and uses it
    Stronger signals? No problem!
It's a lot like an RFID tag
  In a lot of ways it is an RFID tag
  In other ways...not so much :)
NB: “RFID” = “Contactless” = “NFC” = “WTFEver”.
  As long as it's at 13.56MHz

## Slide 5: GuardBunny vs RFID
 |  | MIFARE Classic | iClass
Passively powered, active device | ✔ | ✔ | ✔
Communicates via load modulation | ✔ | ✔ | ✔
Memory | 4 bits | Up to 4K | Up to 4K
Non-volatile storage | ✘ | ✔ | ✔
Has CPU | ✘ | ✔ | ✔

## Slide 6: Flow of Operation

## Slide 7: Why a 4-bit counter?
ISO 14443 specifies an ~847KHz subcarrier
  A.K.A. fc/16 = carrier frequency / 16
  1 bit duration = 8 periods of the subcarrier
In these systems fc/16 is critical
4 bit counter = 16 possible states
16 states into a modulator gives you fc/16
GuardBunny speaks ISO14443! :)

## Slide 8: So what’s with the fc/16?
The tag communicates via fc/16
GuardBunny outputs fc/16
GuardBunny doesn't have to be loudest
  If it can flip a single bit, it wins
  If it can de-sync the reader's timing, it wins
  If it can confuse the reader at all, it wins
Loud enough to be heard is good enough.

## Slide 9: Electrical

## Slide 10: Schematic

## Slide 11: Stage 1: Antenna
Nothing too special
Shorted for the PCB layout
  Electrically, it kinda is
Tuning is tricksy.
  But critical!
  Use another PCB to tune.

## Slide 12: Stage 2: Power Supply
Two halves of a full-wave rectifier
  The middle line is “ground”
C1 & C3 decouple the supply
D2&4 compensate for D1&3
  While doubling voltage
  2 phases doubles voltage again
C2 & C4 are tanks
LED1 & 2 act as voltage limiters
Very low drop-out

## Slide 13: Stage 3: 4-bit counter
74LV163, but any binary counter is fine
Key specification rating: Turn-on voltage
  (74LV is 2V)
Check datasheets for weird pins
Make sure it'll take a 13.56MHz clock...

## Slide 14: Stage 4: Modulator
“Analog switch”
Switching speed and voltage rating are crucial
When E is high, short Y and Z together.
Y and Z go to coil, E now load-modulates

## Slide 15: Stage 5: Limiter
The counter gets its clock from the coil
If the coil is shorted there is no clock!
Solution: don't short the coil completely.
D5 & D6 guarantee at least 0.7V on the coil

## Slide 16: Schematic Redux

## Slide 17: Demo

## Slide 18: Improvements

## Slide 19: That’s v1. What would v2 look like?
Antenna geometry matching
  PSU trickery
Counter chip input impedance
  Constant-current regulators to the rescue!
Modulator logic
  Different approaches
Power supply
  Switchmode for lower dropout?
Additional alerts

## Slide 20: Capturing the Flux
Magnetic field lines flow through the coil
If coils don't match, not all flux is matched
If flux is mismatched, power is mismatched
Power the tag but not GuardBunny :(

## Slide 21: Solution: Antenna arrays
Use lots of antennas!
Crude: Multiple GuardBunny circuits per instance
Better: give each antenna a PSU, combine in series
Ultimate: Manipulate phase and combine at the antenna.
Once powered, modulate all the antennas as one

## Slide 22: Counter input
Counter chip gets its clock directly from the coil
Not a problem unless power is high
  The LEDs ultimately limit coil voltage
Protection diodes shunt away the excess
  Killing our modulation depth in the process
Loss of good power for no signal benefit

## Slide 23: Solution: Impedance trickery
We want low impedance at low voltage
We want the chip to turn on quickly
We want high impedance at high voltage
We don't want excess voltage reaching the chip
We also don't want power from the coil to be shunted
Simple PSU approaches don’t work!

## Slide 24: Constant current regulator
Converts constant V to constant I
Set I very low (input impedance is known)
Use something better than a 7805
  Some kind of LDO regulator, probably
Output voltage is odd
  Efficiency vs logic thresholds

## Slide 25: Modulator logic
The current logic:
  If PSU is overcharged, discharge through LEDs
  If the modulator is on, short-circuit the coil (+/- lim)
At high energy, too much power goes to LEDs
An alternate approach:
  Allow PSU to charge endlessly
  Modulator dumps power from PSU into LEDs
  PSU recharge current back-propagates to coil
  Phase shifts might cause problems (or fun!)

## Slide 26: Power supply
The present combination works well
  No uncompensated voltage drops, high efficiency, 4x multiplier
Could avoid dumping power to LEDs
  Same constant current trickery as for counter
Could go for a higher multiplier
  Tradeoff: more caps and diodes. Not too bad. Useful?
Switchmode might help low-end performance
  Very tricksy to design
Still might get killed by lack of power

## Slide 27: Alerting options
Extend the counter - bit 10 is audio
  Several good tones at Q10-14, choose or combine
    (Q16 && Q10) || (!Q16 && Q11) == 2-tone siren!
  Drive a piezo with them!
Should be enough power to drive a BLE chip
  Increase PSU caps to stay alive longer if needed
Lots of UI possibilities in a card form factor
  Screen showing event count?
  Button to disable device?

## Slide 28: Failure Modes
Antennas don't match
  Can't ever be perfect. Does “good enough” exist?
Way, WAY too much power
  LEDs will likely die first, releasing PSU voltage
  Chips die pretty soon after == no more fc/16
  Finally, PSU caps are rated at 25V (magic smoke?)
  Use a high-voltage zener to protect against this
    Dies eventually – but so will the tag.
DSP to separate GB modulation from tag
Static electricity (the counter chip is sensitive)

## Slide 29: Build

## Slide 30: Build a Batch of Bunnies
It's designed to fit into a clamshell case
  Counter IC is TSSOP – 1.2mm thick
  Flex PCBs will fit, FR4 probably not
Production costs (approx):
  $100 / board in qty 10 (not including assembly)
  $10 / board in qty 1,000 (including assembly)
  $5 / board in qty 10,000 (including assembly)
None of the parts are particularly tricksy
  0603 caps, SOD523 diodes, SOT23-5 modulator

## Slide 31: Component Selection
Tuning caps are sensitive! Use 1%, C0G, 100V
PSU caps not so sensitive. 10V+, 0.1uF+
Diodes: Fast recovery is key, ideally a few ns
  1N4148 works fine at 4ns, but could be improved
  Make sure your limiter diode Vf will allow clock to tick!
Counter: Low-voltage turnon is crucial. TSSOP.
  Any old 4-bit binary counter will work though!
Modulator: Check voltage / current ratings.

## Slide 32: Component selection: LEDs
Start by checking voltage ratings on chips
Each LED shunts half the supply voltage
  This sets the maximum forward voltage allowed
Tradeoff: forward voltage
  Higher Vf means GuardBunny is more effective
  Lower Vf means that the LEDs turn on sooner
Tradeoff: forward current
  Higher If means brighter lights
  Lower If means more effective but vulnerable to high power

## Slide 33: Conclusions
It's a v1, proof-of-concept device.
It works, but has (fixable) weaknesses
My opinion:
  Not yet worthy of selling as a product
  Definitely worthy of talking about :)
Lots of work to do – help appreciated!

## Slide 34: Questions?
Schematic, layout, BOM, gerbers, logos etc:
https://github.com/kristinpaget/GuardBunny